## Slide 1
ANSI Tables
OC Curve

## Slide 2
There are three methods to calculate the probability of acceptance:
Hyper-geometric
Binomial
Poisson
distribution methods.
(https://accendoreliability.com/oc-curve-with-binomial-method/)

## Slide 3: Binomial

## Slide 4: Binomial
Variasi Exactly Peluang Head pada 1 Kesempatan Toss Koin | 
 | Iteration Count: 100_000
Probability Mass Function
number_s=k, trials=n, probability_s=p

## Slide 5
Variasi Exactly Peluang Head pada 6 Kesempatan Toss Koin | 
 | Iteration Count: 100_000
Binomial Probability Mass Function

## Slide 6
 |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 1 |  |  |  |  |  | 
 |  |  |  |  | 1 |  | 1 |  |  |  |  |  |  | 2 |  |  |  |  |  |  | 0.5 |  | 0.5 |  |  |  |  | 
 |  |  |  | 1 |  | 2 |  | 1 |  |  |  |  |  | 4 |  |  |  |  |  | 0.25 |  | 0.5 |  | 0.25 |  |  |  | 
 |  |  | 1 |  | 3 |  | 3 |  | 1 |  |  |  |  | 8 |  |  |  |  | 0.125 |  | 0.375 |  | 0.375 |  | 0.125 |  |  | 
 |  | 1 |  | 4 |  | 6 |  | 4 |  | 1 |  |  |  | 16 |  |  |  | 0.0625 |  | 0.25 |  | 0.375 |  | 0.25 |  | 0.0625 |  | 
 | 1 |  | 5 |  | 10 |  | 10 |  | 5 |  | 1 |  |  | 32 |  |  | 0.03125 |  | 0.15625 |  | 0.3125 |  | 0.3125 |  | 0.15625 |  | 0.03125 | 
1 |  | 6 |  | 15 |  | 20 |  | 15 |  | 6 |  | 1 |  | 64 |  | 0.015625 |  | 0.09375 |  | 0.234375 |  | 0.3125 |  | 0.234375 |  | 0.09375 |  | 0.015625
Pascal’s Triangle

## Slide 7
Variasi Exactly Peluang “Enam” pada 1 Kesempatan Roll Dadu | 
 | Iteration Count: 100_000
Binomial Probability Mass Function
number_s=k, trials=n, probability_s=p

## Slide 8
Variasi Exactly Peluang “Enam” pada 3 Kesempatan Roll Dadu | 
 | Iteration Count: 100_000
Binomial Probability Mass Function
number_s=k, trials=n, probability_s=p

## Slide 9
Variasi At Least Peluang “Enam” pada 3 Kesempatan Roll Dadu | 
 | Iteration Count: 100_000
Binomial Cumulative Distribution Function
number_s=k, trials=n, probability_s=p

## Slide 10
Peluang Muncul Maximum Dua “Enam” pada n Kesempatan Roll Dadu | 
 | number_s=k, trials=n, probability_s=p
Binomial Cumulative Distribution Function

## Slide 11
OC Curve n = 8 # jumlah sample dari lot, k = 2 # jumlah defects bisa diterima | 
 | Iteration Count: 100_000
Binomial OC Curve

## Slide 12
OC Curve n = 8 # jumlah sample dari lot, k = 0 # jumlah defects bisa diterima | 
 | Iteration Count: 100_000
Binomial OC Curve

## Slide 13: Poisson

## Slide 14: Poisson
Average daily questions = 4, how likely to have exactly 7 questions? https://www.youtube.com/watch?v=BbLfV0wOeyc | 
 | x = k, mean = lambda
Probability Mass Function

## Slide 15
Average daily questions = 4, how likely to have maximum 7 questions? https://www.youtube.com/watch?v=BbLfV0wOeyc | 
 | x = k, mean = lambda
Poisson Cumulative Distribution Function

## Slide 16
How likely to have maximum 7 questions, with various average daily questions? | 
 | x = k, mean = lambda
Poisson Cumulative Distribution Function

## Slide 17
OC Curve n = 8 # jumlah sample dari lot, k = 2 # jumlah defects bisa diterima | 
 | Iteration Count: 100_000
Poisson OC Curve

## Slide 18
OC Curve n = 8 # jumlah sample dari lot, k = 0 # jumlah defects bisa diterima | 
 | Iteration Count: 100_000
Poisson OC Curve

## Slide 19: OC Curve: Binomial vs Poisson vs Stochastic vs ANSI Tables

## Slide 23
Key definitions
The Operating Characteristic (OC) curve is a curve showing, for a given sampling plan, the probability of acceptance of a lot as a function of it’s actual quality.
Producer’s Risk is the probability of wrongly rejecting a compliant lot, with level of non-conformance at or below the acceptance quality limit (or proportion of non-conforming units for lots consisting of discrete items). Generally the quality of an acceptable lot is expressed as the Acceptance Quality Limit. It is a point on the OC curve corresponding to some predetermined and usually low probability of rejection. This probability of rejection is called the ‘producer’s risk’.
Consumers’ Risk is the probability of wrongly accepting a lot that is not of acceptable quality. It is a point on the OC curve corresponding to a predetermined and usually low probability of acceptance. This probability is then called the ‘consumer’s risk’ and the corresponding lot quality is called the Limiting Quality (LQ or LQL).
The Acceptance Quality Limit (AQL) (previously called Acceptable Quality Level) is the level of proportion of non-conforming items at which lots are accepted most of the time, usually taken as 95%.
The Limiting Quality (LQ or LQL) is the proportion of non-conforming items associated with the consumer’s risk, or the level of non-conforming items of lots accepted after control, in 10% of the cases.
https://www.massey.ac.nz/~kgovinda/nzcodexdoc/index.html
 | Accept The Lot | Reject The Lot
Good Lot | No Error | Type I Error Producer’s Risk
Bad Lot | Type II Error Consumer’s Risk | No Error
 | Sampling Error | 

## Slide 24
n | p | x | lambda | Poisson CDF
50 | 0.01 | 2 | 0.5 | 0.986
50 | 0.016361 | 2 | 0.818045 | 0.950
50 | 0.02 | 2 | 1 | 0.920
50 | 0.03 | 2 | 1.5 | 0.809
50 | 0.04 | 2 | 2 | 0.677
50 | 0.05 | 2 | 2.5 | 0.544
50 | 0.06 | 2 | 3 | 0.423
50 | 0.07 | 2 | 3.5 | 0.321
50 | 0.08 | 2 | 4 | 0.238
50 | 0.09 | 2 | 4.5 | 0.174
50 | 0.1 | 2 | 5 | 0.125
50 | 0.106405 | 2 | 5.320267 | 0.100
50 | 0.11 | 2 | 5.5 | 0.088
50 | 0.12 | 2 | 6 | 0.062
Producer’s Risk:
alpha = 0.05, AQL=1.64%
Consumer’s Risk:
beta = 0.1, LQ=10.64%

## Slide 25
alpha = 0.05, AQL=0.172
beta = 0.1, LQ=0.835
n | p | x | lambda | Poisson CDF
8 | 0.01 | 3 | 0.08 | 1.000
8 | 0.05 | 3 | 0.4 | 0.999
8 | 0.1 | 3 | 0.8 | 0.991
8 | 0.15 | 3 | 1.2 | 0.966
8 | 0.2 | 3 | 1.6 | 0.921
8 | 0.171581 | 3 | 1.3726 | 0.949
8 | 0.25 | 3 | 2 | 0.857
8 | 0.3 | 3 | 2.4 | 0.779
8 | 0.35 | 3 | 2.8 | 0.692
8 | 0.4 | 3 | 3.2 | 0.603
8 | 0.45 | 3 | 3.6 | 0.515
8 | 0.5 | 3 | 4 | 0.433
8 | 0.55 | 3 | 4.4 | 0.359
8 | 0.6 | 3 | 4.8 | 0.294
8 | 0.65 | 3 | 5.2 | 0.238
8 | 0.7 | 3 | 5.6 | 0.191
8 | 0.75 | 3 | 6 | 0.151
8 | 0.8 | 3 | 6.4 | 0.119
8 | 0.834984 | 3 | 6.6799 | 0.100
8 | 0.85 | 3 | 6.8 | 0.093